## Slide 1: MEG Neuroimaging: “spatiotemporal imaging”
MEG lab: Clarkson Doctors building – South
Valentina Gumenyuk, PhD
November 10, 2022
MEG core CoNDA Neuroimaging Great Plains IDeA-CTR Network

## Slide 2
Evolution of the MEG

## Slide 3
Spatial – Temporal resolution and Invasiveness
http://web.mit.edu/kitmitmeg/whatis.html

## Slide 4
MEG equipment
(Hamalainen 1993)
Modern standard MEG equipment, FDA cleared
First MEG (1967)
Professor in Radiology,
Harvard Medical School
“The Father of the MEG” Dr. David Cohen
1 MEG sensor
37 MEG sensors
306 MEG sensors

## Slide 5
Schematic illustration of the modern MEG system

## Slide 6: Current Generation of the “MEG helmet”
Consequently, SQUIDs are suitable for
the detection of brain’s magnetic fields ranging from DC
[that is,0 Hz] to 1000 Hz and above.
OPM (Optically Pumped Magnetometers)
system at Martinos Center
Yoshio Okada
Matti Hämäläinen
Improvements :
High sensitivity (finally) reached
  Still needs cryogens
  Mass production of sensors with uniform quality
  Simultaneous recording of group of subjects
Triux

## Slide 8
MEG opportunities in Clinical and Research studies

## Slide 9: MEG method was designed for Noninvasive Evaluation of Brain Activity
From the very beginning, MEG analysis has emphasized the need for modeling of sources of neuronal brain activity elicited at
HIGH temporal resolution !
somatosensory ( at 25 – 30 ms after stim), motor (at 50-80 ms), auditory mid /long latency (at 50 ms), language processing (at 280-600 ms), epileptic spike (peak <70 ms)

## Slide 10
What MEG +EEG / MEEG results can reveal?

## Slide 11
MEG measure brain signal in 3D space
MEG brain signal measures noninvasively in millisecond time scale
The brain MEG sources can be functionally characterized by their:
locations, orientations, time courses, and strengths
of the source
“SOURCE ESTIMATION”
(MEG data analysis)
MEG Data provides information about the location in 3D space for each millisecond time point

## Slide 12
EEG Cap
Head Digitization
~ 40 min
~ 15 min

## Slide 13
Good MEG results require a good recipe :

## Slide 14
MEG DATA: Pre-Processing

## Slide 15
Parametric models
  Assume a limited number of dipoles
  Overdetermined: more measurements than source parameters
Current distribution models
  Many sources in a volume or on a surface
  Need an additional constraint: minimize a norm of the current distribution while matching the data
  MNE: overall power minimized
SOURCE ESTIMATION can be performed:

## Slide 16: Are dipoles good for extended sources?
Activated area
Best-fitting dipole
gof = 99.9%
Matti Hämäläinen
Auditory N100m

## Slide 17
MEG dipoles results
Surface EEG dipoles results
Patient with Temporal lobe Epilepsy
Spatial resolution MEG vs. surface EEG:
J Ebersole : Epilepsia, 1997
EEG resolution in cm -range
MEG resolution in mm - range

## Slide 18: Visual Stability During Eye Blinks
Hari et al., Nature, 1994
MEG field to the “blink”

## Slide 19
Somatosensory MEG responses evoked by electric stimuli delivered to the subject left thumb
Lounasmaa et al., 1996

## Slide 20: Spatial-Temporal Dynamic Of Cortical Activity in picture naming task

## Slide 21
Mission-S of the MEG lab:
Clinical evaluation (MEG IMAGING) of patients with the brain disorders that can be surgically treated
Epilepsy
Tumor
Arteriovenous brain malformations (AVMs)
Brain hemorrhagic lesion
Research studies
(ongoing & planned):
Develop clinical tool for the MEG imaging
Normal and Abnormal Aging
Auditory Cognition
Auditory-Motor Integration (Voice control)
Abnormal Irritability (Dr. Hwang, Department of Psychiatry)
Impact of Leukemia Treatment on cognitive ability (Dr. Bhatt, Division of Hematology-Oncology)
Social interaction (Dr. Chen)
Music therapy (Dr. Phatak)
Sleep: (Sleep onset & Physiological arousal)

## Slide 22
Education and Training in the MEG field medical/research fellows:
To understand the MEG Imaging with respect to other modalities
Learn what the MEG applications for clinical and research studies
Teaching MEG data collection /data analysis
Learn how to build the successful MEG study from the design of the study to the manuscript writing

## Slide 23
Presurgical Evaluation of the Dominant Hemisphere function in an adolescent patient with Rasmussen’s Encephalitis using MEG
Diffuse microglial activation and scattered microglial nodules (arrow) with foci of neuronophagia (inset, hematoxylin & eosin)
PET
Histology
EEG results study in awake

## Slide 24
Temporal resolution MEG vs. surface EEG:
Receptive Language Mapping:
Auditory Passive Listening Task during sleep
Right hemisphere was more involved in the processing
of spoken words
Dr. Spriha Pavuluri
Instructor (Department of Neurological Sciences)

## Slide 25
EEG epileptic spike has a
peak amplitude duration <70 ms
EEG study is a Standard Procedure to evaluate the epileptogenic activity and its origin

## Slide 27
Spatial and Temporal Dynamic of Epileptic MEG spike
Dr. Daniel Zhou
(PGY4 resident, Neurology program)
Manuscript in preparation

## Slide 28
Standard MEG clinical results: Interictal spikes localized in right and left occipital areas
Results of Granger Causality connectivity
LEFT spikes showed bilateral propagation
Patient is seizure free for 1 year and 7 mo, her vision is stable and remains intact
R occipital
L occipital

## Slide 29
Motor evoked field to movement of the LEFT Hand
MEG response at 50 ms

## Slide 30
Sensory (air puff) evoked field to the LEFT Leg (above heel area)
MEG response at 150 ms

## Slide 31
InterIctal activity propagation within 10 ms
Sensory LEFT LEG
Motor movement LEFT Hand

## Slide 32
Currently Ongoing Research Projects

## Slide 33
Jack CR, et al. Lancet Neurol 2010: Dynamics of Biomarkers in AD
PET & MRI [metabolomic and anatomical level]
are much less sensitive to measure the neuronal dynamics (changes due to synapse damage, or impairment in axonal conductance) with respect to signal-based method
(MEG, EEG and ERPs).
Objectives:
Lack of biomarker – measuring the magnitude and slope (rate of changes) of the disease at a given point in time
Lack of biomarker – capturing the abnormal neuronal processing in high temporal resolution
Lack of biomarker- measuring the impact of disease non-invasively; and the drug-induced changes in response to the treatment
Available biomarkers (AD)

## Slide 34
Brain Changes in Dementia (AD)
Build – up of amyloid – beta peptide plaques in the brain
Gradual intracellular accumulation of neurofibrillary tangles (NFT) in brain neurons
Cortical lesions in AD are associated with accumulation of NFT in the medial temporal lobes
Cognitive changes in AD are strongly associated with the accumulation of NFT (Nelson et al., 2012)
Healthy Control
Asymptomatic
Alzheimer’s Disease
Dementia
From Dr. Daniel Murman * grand rounds sept 2021*

## Slide 35
Structural and MEG results in Left temporal atrophy
(65 y.o., female)
Gumenyuk et al., in preparation
MEG focal slowing

## Slide 36
Previous studies have been demonstrated that the MMN brain response is suitable tool for differentiation between frontal and temporal brain activity.
According to the modern Predictive processing theory the MMN is reflecting the error detection in predictive auditory processing.
In addition to temporal lobe generator, the MMN response activates the frontal lobe areas that are important for the goal of our dementia MEG study.
MMN is a cognitive brain response to change detection. In auditory modality, MMN elicited at 150-200 ms after
change onset

## Slide 37
Results of this MEG study showed:
FT-d group has suppression of frontal and temporal brain activity in auditory change detection response (latency at ~150-200 ms) with respect to healthy controls
J Cogn Neurosci. 2013

## Slide 38
Korzyukov et al., 2003
Gumenyuk et al., 2003
Paradigm for the abstract –rules in auditory passive task
Duration : 23 minutes

## Slide 39
Results of MMN brain localization
*control subject (67 y.o.)*
Temporal source of MMN at 170 ms
Frontal source of MMN at 214 ms
MEG waveforms
T
F

## Slide 40
Temporal- Frontal neuronal activity in auditory processing:
Subject is healthy 67 y.o. female

## Slide 41
MEG study of Sleep disturbances

## Slide 42
Habitual sleep – wake evaluation via actigraphy and sleep log
Control subject
Female, 67 y.o.
Dementia Lewy Body subject
Female, 71 y.o.
Disturbed wake-sleep cycle
Circadian rhythm misalignment

## Slide 43
Volunteer with permission
During sleep some brain activity is magnified at sensor and source level, but the origin of the source remains the same
Gumenyuk et al, in preparation

## Slide 47
MEG results are replicable !

## Slide 48: SUMMARY:
MEG and EEG directly measure the activity of the neurons providing complementary information
Both methods have excellent temporal resolution but MEG outperforms EEG in the spatial resolution
MEG results replicated across the different MEG laboratories
MEG results can guide the intracranial EEG study
MEG method could be combined with other Imaging techniques :
MEG + EEG or MEG + TMS + EEG or multiple MEGs (OPMs)

## Slide 49
MEG Imaging is FUN -Imaging !
THANK you All!